## Slide 1: PANDA Magnets
Template for presentations concerning the magnet design at PANDA

## Slide 2: Spectrometer Magnets at PANDA
Prerequisite for momentum reconstruction and PID
Ideal combination
  2T central solenoid field
  1T forward dipole field
Technical Design Report (reviewed May 2009): arXiv:0907.0169

## Slide 3: Superconducting Solenoid
Challenges
  2T field
  4m x 1.9m free space
  High field homogeneity
  Target pipe intersection
  Access on both sides
  Movement by 20m
  Muon range system
Central field 2.0 T
Field homogeneity ≤2%
Norm. radial field integral ≤2 mm
Inner bore 1.9 m
Cold mass parameters
Length 2.7 m
Energy 20 MJ
Current 5000 A
Weight 4.5 t
Cable cross section 3.4 × 2 mm2
Current density 59 A/mm
Yoke parameters
Length 4.9 m
Outer radius 2.30 m
Iron layers 13
Total weight 300 t

## Slide 4: Superconducting Solenoid
Flux Return Yoke
  shape homogeneous field
  muon range system
    barrel: 13 layers
    forward doors: 5 layers
  opening doors
  accommodate target
  retractable to parking position (20m)
  reproducible positioning

## Slide 5: Superconducting Solenoid
Coil
  Internally wound on mandrel
  Al stabilised Rutherford cable
  split coil: 3 sections allowing target intersection
  indirect cooling
Cryostat
  asymmetric warm bore
  mounting structure for detectors

## Slide 6: Large Aperture Dipole
2Tm for particles scattered in 0 – 10o (5o vertical)
Allows momentum resolution <1%
Large aperture (1x3m) and short length (2.5m)
Ramping capability due to lamination
Field integral 2 Tm
Bending variation ≤ ±15%
Vertical Acceptance ±5°
Horizontal Acceptance ±10°
Ramp speed 1.25%/s
Total dissipated power 360 kW
Total Inductance 0.87 H
Stored energy 2.03 MJ
Weight 220 t
Dimensions (H × W × L) 3.88 × 5.3 × 2.5 m3
Gap opening (H × W) 0.80 − 1.01 × 3.10 m2