## Slide 1
The Central Straw Tube Tracker In The PANDA Experiment
Peter Wintz (IKP - FZ Jülich), for the PANDA collaboration
11th International Conference on Low Energy Antiproton Physics,
June 10-15, 2013, Uppsala, Sweden

## Slide 2
PANDA physics
Central Straw Tube Tracker (STT)
  Minimal material budget
  High-rate tracking and PID
  Online event reconstruction ( next talk)
Test systems and results
Simulation studies
Summary
Outline: PANDA - Straw Tube Tracker

## Slide 3
PANDA investigates pp and pA annihilation in the charm quark mass regime
Hadron spectroscopy (m, G, JPC, BR)
  Charmonium states
  Open charm mesons (D-mesons)
  Exotic states (glueballs, hybrids, multi-quarks)
  Strange and charmed baryons
Hadrons in nuclear medium
  J/y - absorption, D meson mass shift
  Hypernuclei (X-AZ, LLAZ), YY-interaction
Structure of the nucleon
  Electromagnetic formfactors
  Generalized Distribution Amplitudes
  Transverse nucleon spin (full PWA)
_
_
2.25 < s < 5.47 GeV
PANDA Physics Performance Report
arXiv:0903.3905 (216pp)
The PANDA Physics Program
_
 Talks by A. Gillitzer (Tue), A. Sanchez (Wed), M. Maggiora, B. Kopf (Thu)

## Slide 4
The PANDA Detector System In HESR
d
d
Forward spectrometer,
2Tm dipole magnet
Target
spectrometer,
2T solenoid
13m
_
 Talk by D. Calvo

## Slide 5
Variety of event topologies, all particle species involved
  particle multiplicities up to 6 and higher, on average ~150 tracks / 2µs
  broad momentum range ~ 100 MeV/c - 8 GeV/c
  displaced vertices O(100µm) - O(10cm)
4p solid angle coverage (PWA)
High momentum & spatial resolution: σp/p~1-2%, vtx ~50µm
Particle identification: p/K/ <1 GeV/c (exclusively)
Readout of (quasi-) continuous data stream
  fast online track & event reconstruction, w/o t0, evt. deconv.
  flexible software triggering, specific reactions  data storage
Tracking system: MVD (vertex) + Central Tracker (large-vol) + GEMs (forwd)
Tracking At PANDA
Simulation

## Slide 6
4636 straw tubes in 2 separated semi-barrels
23-27 radial layers in 6 hexagonal sectors
  15-19 axial layers (green) in beam direction
  4 stereo double-layers: ±3° skew angle (blue/red)
Volume: Rin / Routr= 150 / 418 mm, L~ 1650 mm
  Inner / outer protection skins (~ 1mm Rohacell/CF)
Ar/CO2 (10%), 2 bar, ~ 200ns drift time (2 T field)
Time & amplitude readout
  sr ~ 150 µm, sz ~ 2-3 mm (isochrone)
  (dE/dx) < 10% for PID (p/K/ < 1 GeV/c)
p /p ~ 1-2% at B=2 Tesla (STT + MVD)
X/X0 ~ 1.25% (~ 2/3 tube wall + 1/3 gas)
Central Straw Tube Tracker (STT)
STT x-y view
STT 3d-view

## Slide 7
Material budget at lowest limit (2.5 g per assembled straw)
thinnest Al-mylar film, d=27µm, =10mm, L=1400mm
thin-wall endcaps (ABS), wire fixation (crimp pins), radiation-hard
self-supporting modules of pressurized straws (p=1bar)
  close-packed (~20 µm gaps) and glued to planar multi-layers
  replacement of single straws in module possible (glue dots)
strong stretching (230kg wires, 3.2tons tubes)*, but no reinforcement needed
Straw Tubes
Straw components
IKP FZ Jülich
Full hexagon sector
* Sum for 4600 straws in the PANDA-STT
IKP FZ Jülich

## Slide 8
.. technique first developed for COSY-STT (planar double-layers, in vacuum!)
.. upgraded for PANDA-STT (barrel geometry with 3d stereo-layers, quad-layers)
Self-Supporting Straw Modules
3kg Pb brick on 27µm
Mylar
Pressurized, close-packed straw layers show a strong rigidity ..

## Slide 9
STT Mechanical Prototype
STT mechanical prototype, one semi-barrel
Even more confidence in the self-supporting straw modules through the years ..
.. 33kg!
Full hexagon sector, overpressure 1 bar

## Slide 10
Mechanical Frame Structure
CABLE ROUTING TRAY SUPPORT STRUCTURE (CRFP)
MAIN GAS PIPES (Rilsan)
ELECTRONICS PATCH PANELS (Aluminum)
ELECTRONICS CARDS
ELECTRONICS CARDS PROTECTION SKIN (Kevlar)
STRAW TRACKER OUTER
PROTECTION SKIN (Kevlar)
CABLES ROUTING TRAY (Aluminum)
Sketch of frontend part
INFN Frascati
STRAW MODULE
MECHANICAL FRAME (UPSTREAM)
ANALOG READOUT
CARD
STRAW MODULE
SUPPORT
HIGH VOLTAGE DISTRIBUTION
GAS MANIFOLD

## Slide 11
Final Assembly Scheme
INFN Frascati + Torino
Central frame structure to support all central components
  beam pipe + MVD + STT semi-barrels
Rail system for insertion into the PANDA target spectrometer

## Slide 12
2 Concepts to measure drift time + signal amplitude (for dE/dx)
  Amplitude sampling: LE-Time + Q
  Amplifier-shaper boards frontend at detector
  Pulse sampling by FADC (240 MHz), pulse analysis and readout by FPGA
  Amplitude by time-over-threshold*: LE-Time + ToT(Q)
  Ampl.-Shaper-Discr. (ASIC-chip) frontend at detector
  Time Readout Boards (TRB), TDC in FPGA
Requirements
  ~ 2fC sensitivity (thresh. ~ 1.2104 e-)
  ~ 1ns time resolution, ~ 200ns drift time range for Ar/CO2(10%) at 2 T field
  < 10% dE/dx resolution for PID
  Hit rates: ~ 800 kHz/straw (max), ~ 400 kHz (avg.) at full luminosity
FEE must be radiation-hard, low power consumption, minimum space
STT Readout
Design by AGH Krakov
(CMOS 0.35µm)
*ToT used for PID at
ATLAS-TRT & HADES-MDC

## Slide 13
STT semi-barrel (1:1) for assembly techniques
Mechanical central frame structure on rail system
STT detector in COSY-TOF experiment
  “Global“ test system for PANDA-STT (straw technique)
  Spatial resolution:  ~ 140µm (2700 straws)
  Operated (4 yr) in evacuated time-of-flight barrel (25m3)
  Leakage on permeation level (molecular flow thru mylar)
Straw setups for in-beam tests (p/d-beam)
  Aging tests done, charge loads ~1.2 C/cm (~ 5yrs PANDA)
  High-rate readout tests ongoing, 1-2 MHz/straw
  Beam momentum 0.6 - 3 GeV/c (dE/dx range ~ 3 mips)
Test Systems

## Slide 14
dE/dx resolutions measured in beam with FADC
  dE/dx = 7.0% - 9.3% (0.6, 1.0, 2.9 GeV/c protons)
  30% truncation factor (Landau-tail)
  < 19 straw hits per track  25 layers at PANDA-STT
dE/dx ~ 7.0 % feasible with PANDA-STT
 ~ 150µm spatial resolution measured
High-rate FPGA analysis & readout ongoing
FADC Energy-Loss Measurements
1-2 MHz/straw

## Slide 15
Time (ns)
Time over Threshold (ns) 
ASIC testversion with analog out, first in-beam test 2012
  gain (3-24mV/fC), peak time (20/40ns), ion tail cancell., BL stability, ..
Next ASIC version in production: 100 chips 8 ch, few param. optimisations
Calibration of ToT  dE/dx with 55Fe-source (simple) and beam protons
  need >4 different beam momenta to get ToT  dE/dx relation and resolution
Time-Over-Threshold Method
Pulse
integral
ToT
(25mV)
ToT
(50mV)
Beam on straws, TRB readout
50mV threshold
25mV threshold
dQ/Q resolution ~ 10%
Charge (pC) vs ToT(ns)
backgrd
55Fe-signals, 220(110)e-/200µm,
pulse integral + ToT measuremt

## Slide 16
Single track simulation (MVD+STT+GEM, B=2T)
  Momentum resolution 1-2% for  < 140°
Test of tracking system with benchmark channels
  vertex resolutions and reconstructed
  mass of D-mesons
Simulation Studies
D-meson reconstruction numbers

## Slide 17
The PANDA-STT provides a complete measurement of charged particles: space, momentum, pid, (time)
Test measurements and benchmark channel simulations confirm the required performance
Technical design report of the STT was approved in 2012
Funding process will be completed soon (Germany, Italy, Poland, Romania)
Straw mass production during 2013-2016 (> 50% spares)
Electronic readout optimisation in parallel, beam test times at COSY
Comissioning of the detector setup with beam in 2016/2017 at COSY
Shipping to FAIR and installation in PANDA 2017
Summary
Technical design report of the PANDA-STT, Eur.Phys.J.A49 (2013) 25