Subsystem: Micro Vertex Detector

Subsystem structure

The Micro Vertex Detector (MVD) consists of two silicon devices: hybrid silicon pixels and double sided silicon micro-strips.
Four barrels, two innermost composed of hybrid pixels and two outermost composed of micro-strips, are located around the interaction point. Six disks based on hybrid pixels and two micro-strips rings compose the forward part of the MVD.

The readout electronics for both pixels and micro-strips is custom due to the challenging request of a trigger-less readout.

The readout of the pixels is based on the chip named ToPix, bump bonded to the sensor.
A ToPix chip implements a 12760 pixel readout channel matrix and includes two drivers which transmit data at 320 Mb/s each.
The pixel module layout is based on a basic unit corresponding to a readout chip size and modules of several sizes are obtained by tiling from two to six units.
In total, 176 sensors and 810 readout chips equip the pixel detector (10335600 readout channels): 64 sensors and 338 chips in the barrels (4312880 readout channels), 112 sensors and 472 chips (6022720) in the disks.

The readout ASIC of the strip part is named Toast (new prototype of the PASTA project that did not meet the specifications) and implements 64 readout channels.
The strip part foresees 3 different geometries: square sensor, readout by 8 ASICs each, and rectangular, readout by 11 ASICs each, equip the two barrels and trapezoidal sensors, readout by 12 ASICs each, compose the two rings.
In total, 296 sensors and 3112 chips equip the micro-strips detector (199168 readout channels): 64 square and 184 rectangular sensors and 2536 chips in the barrels (162304 readout channels), 48 trapezoidal sensors and 576 chips in the rings (36864 channels).
Data from Toast chips are handled by a Module Controller Chip (MDC), one chip for each sensor for a total number of 296 MDC chips.

Readout architecture and data transmission for the pixel detector

Dedicated optoelectronic board, composed of a GBT chip-set and a Versatile link (generically indicated as GBT), both developed at CERN for the LHC projects, reduces the electrical data transmission lines in favour of fast optical data links. 320 Mb/s serial links, based on the SLVS (Scalable Low Voltage Signaling) differential standard, in order to be compatible with the 1.2 V voltage supply typical deep sub-micron technologies, interface the GBT to the front-end electronics.
68 GBT for the barrels and 95 GBT for the disks will be arranged immediately in front of the MVD.

The MVD Multiplexer Board (MMB) is the off-detector electronic based on Advanced Mezzanine Cards (AMC) for microTCA that will manage data from up to 3 GBTs and send them to the FPGA-based Compute Nodes of the DAQ system, using a 10 Gb/s optical link. In addition, it receives the clock signal from the time distribution system of the experiment (SODA).
23 MMB boards for the barrels and 32 MMB boards for the disks complete the data transmission architecture.

Readout architecture and data transmission for the micro-strips detector

D.....

Expected hit rates

The expected particle distribution in antiproton-proton collisions obtained with 107 Dual Parton Model (DPM) events at two different beam momenta (p beam) are reported in figure 1. This distribution is mainly peaked in the forward direction, where the pixel disks and the strip rings are positioned.

Figure 1. In the top of the figure, particle distributions are reported as a function of particle momentum and polar angle. In the bottom part of the figure the 1D profile is projected onto the polar angle. The red line results from the elestic scattering process that is implemented in the DPM generator.

The expected particle distribution in antiproton-nucleus collisions obtained at maximum beam momenta (p beam) are mainly distributed in the angular range covered by barrels part of the MVD as presented in figure 2.

Figure 2. In the top of the figure, particle distributions, obtained with 4 x 104 UrQMD events, are reported as a function of particle momentum and polar angle for antiproton-N and antiproton-Au collisions. In the bottom part of the figure, the 1D profile is projected onto the polar angle, obtained with a statistical sample of 2 x 106

Main results of the count rate study performed with 2 million of DPM events are reported in Table 1.

Table 1. The count rates at the MVD level obtained from the simulation of 2 million of DPM events. Average count rates are obtained with the nominal interaction rate of 2 x 107 s-1, i.e. <Ndig> = 10 Ndig s-1. The numbers reported at sensor, front-end and channel level represent the maximum values obtained for a single element. Mean values of all elements in the corresponding setup are indicated within brackets.