Hough transformations
of DIRC images
Goal: get PID information as early as possible (Trigger)
Hough transformation:	solve linear equation	(fast)
Other procedure:	make a fit	(slow)

---
Results from
PANDAROOT
X [cm]
Kaon	0.6 MeV/c
q = 135 deg.
SiO2
NLAK33
SiO2
Y [cm]

---
given
z0
x1/y1
...
x5/y5
result
Radius
x0=1	theta	= 30
y0=2	phi	= 45
z0=4	psi	= 45
(R = z0*tan psi = 4)

---
62 photons
C625=7*106
expected
R [cm]

---
same particle,
other event
???

---
Hough results are promising
Unclear if simulations generate right images