## Slide 1: Y. Ma D. Rodríguez Piñeiro J. Sánchez Rosado G. Tejerina Álvarez I. Zimmermann HIM/GSI/Mainz University PANDA Collaboration Meeting KVI 31. 08. 2010
PANDA Collaboration Meeting
BW Endcap of EMC Prototype

## Slide 2
1.– Prototype Set-Up
2.– Thermal Studies
3.– Supporting Parts
4.- Summary

## Slide 3
1.– Prototype Set-Up

## Slide 4
20 Crystals Available
16 Fully Equipped
Prototype Goals:
Test Crystals with BW Endcap Geometry
Get Real Feeling of the BW Building It
Due the Tight Space and Low Energy of the Detector Checking: Insulator (Vacuum Panels), Cooling (Front)…
Supporting Parts (Alveoles, Mounting Plate, Feet…)
Many Others (Optic Fibres, Geometries, Construction Details…)
2 Steps: 16 Crystals Subunit – Full Arrangement

## Slide 5
CF Alveoles
Al Inserts
Preamps Support
Preamplifiers
Positioning Frames
Capsules
APDs
Crystals
First Step: Tests at Room Temperature (Strength Test, APDs, Optic Fibers…)
Also Cooling Down the Crystals

## Slide 6
Crystals Dummies
Dummies
Optic Fibres
16 Equipped Crystals
4 Remaining Crystals
Mounting Plate
Second Step: Full Arrangement

## Slide 7
Vacuum Gauges
Vacuum Panels
N2/Vacuum Pipes
Mounting Plate 2
Supporting Feet
Scale Construction 1:1; Real Feet and Cooling (Resistors Simulating the Preamplifiers Heat will Be Placed)
Vermiculite Granulate
Temperature Humidity Sensors

## Slide 8
2.– Thermal Studies

## Slide 9
Crystals in the Middle: Thermal Load Front
∆T=1,41ºC
Crystals in the Border: Thermal Load Front/Side
∆T=6,42ºC

## Slide 10
Crystals in the Middle: Thermal Load Front
∆T=0,35ºC
Crystals in the Border: Thermal Load Front/Side
∆T=1,08ºC
Crystals Wrapped with 100 µm Copper
Physics Simulations with Copper Will Be Performed

## Slide 11
3.– Supporting Parts

## Slide 12
Special Supporting Pieces, “feet”
High Strength
Stops Heat Conduction
Allows Shrinking Displacement
Design Following Barrel
Different Arrangement

## Slide 13
Exploded View
Made Out of:
Non Magnetic Stainless Steel
Glass Fiber
Teflon®

## Slide 14
Stainless Steel
Displacement
Structural Stress
Safety Factor >2 Regarding the Elastic Limit
0,00008 mm

## Slide 15
Glass Fiber
Displacement
Structural Stress
0,0005 mm
Safety Factor >12 Regarding the Elastic Limit

## Slide 16
Displacement
Structural Stress
Aluminium Inserts (Fully Loaded)
Safety Factor >10 Regarding the Elastic Limit
0,008 mm

## Slide 17
5.- Summary

## Slide 18
2 Steps: 16 Crystals - Full Scale
Goal: 16 Crystals Equipped
Many Details will Be Checked (Specially in the Front)
Main Design for the Prototype Done
Checking Different Solutions for Cooling with Copper
Summary

## Slide 19
Thank you!
Personal Contact:
d.rodriguezpineiro@gsi.de
Tel: +49 (0) 615971/1634
www-panda.gsi.de