## Slide 1: David Rodríguez Piñeiro GSI Darmstadt PANDA Collaboration Meeting GSI 05. 03. 2009
PANDA
Collaboration Meeting
Backward Endcap Calorimeter
Geometry

## Slide 2: Backward Endcap EMC
1.– Requirements
- Boundary Conditions
- Dimensions
2.– Geometry
- Distance to the target
- Inner Radius
- Beam Cone Angle
- Wedge Hollow
- Pipe flange
3.- Summary

## Slide 3: Backward Endcap EMC
Distance Target-BW Endcap | 560 mm
Maximum Outer Radius | 448 mm
Minimum Inner Radius | 150 mm
Boundary Conditions
1.– Requirements
- Boundary Conditions
- Dimensions
2.– Geometry
3.- Summary

## Slide 4: Backward Endcap EMC
Crystals Dimensions | Straight Geometry
Length | 200 mm
Face | 24,4x24,4 mm (barrel smallest back face crystal)
Picture | 
1.– Requirements
- Boundary Conditions
- Dimensions
2.– Geometry
3.- Summary
Dimensions
Straight Geometry: 0,6284 str

## Slide 5: Backward Endcap EMC
2.– Geometry

## Slide 6: Backward Endcap EMC
Distance from target to crystals 594 mm (560 mm free space)
Limit angle of the barrel is 39º
Minimum outer angle crystal BW endcap 32,246º
There is a maximum gap of 6,754º
So, we would need to shift the BW endcap forwards, leaving a free space of 428,75 mm
Distance to the target (I)
1.– Requirements
2.– Geometry
Distance to the target (I)
Distance to the target (II)
- Inner Radius
- Beam Cone Angle
- Wedge Hollow (I)
Wedge Hollow (II)
Pipe Flange
3.- Summary
Notes: Decir 560+30+2

## Slide 7: Backward Endcap EMC
30% closer to the target; crystals 554
(free distance 520 mm)
Maximum angle outer crystal BW endcap 34,00º
Distance to the target (II)
1.– Requirements
2.– Geometry
Distance to the target (I)
Distance to the target (II)
- Inner Radius
- Beam Cone Angle
- Wedge Hollow (I)
Wedge Hollow (II)
Pipe Flange
3.- Summary
Notes: Decir 560+30+2

## Slide 8: Backward Endcap EMC
Inner Radius
30% less free space (beam pipe-crystals) of Inner Radius, R128 mm
48 crystals gain
1.– Requirements
2.– Geometry
Distance to the target (I)
Distance to the target (II)
- Inner Radius
- Beam Cone Angle
- Wedge Hollow (I)
Wedge Hollow (II)
Pipe Flange
3.- Summary

## Slide 9: Backward Endcap EMC
Beam Cone Angle
Angle trumpet: 15,85º > 15,08º
(30% smaller)
1.– Requirements
2.– Geometry
Distance to the target (I)
Distance to the target (II)
- Inner Radius
- Beam Cone Angle
- Wedge Hollow (I)
Wedge Hollow (II)
Pipe Flange
3.- Summary

## Slide 10: Backward Endcap EMC
Wedge Hollow (I)
Wedge hollow of 20º
Two pieces
424 Crystals
108 less
1.– Requirements
2.– Geometry
Distance to the target (I)
Distance to the target (II)
- Inner Radius
- Beam Cone Angle
- Wedge Hollow (I)
Wedge Hollow (II)
Pipe Flange
3.- Summary

## Slide 11: Backward Endcap EMC
Wedge Hollow (II)
4-side cut
500 Crystals
2 alternatives, same free space:
2-side cut
448 Crystals
1.– Requirements
2.– Geometry
Distance to the target (I)
Distance to the target (II)
- Inner Radius
- Beam Cone Angle
- Wedge Hollow (I)
Wedge Hollow (II)
Pipe Flange
3.- Summary

## Slide 12: Backward Endcap EMC
Pipe Flange
Flange upstream BW endcap
Estimation: 1000 mm from the target
1.– Requirements
2.– Geometry
Distance to the target (I)
Distance to the target (II)
- Inner Radius
- Beam Cone Angle
- Wedge Hollow (I)
Wedge Hollow (II)
Pipe Flange
3.- Summary

## Slide 13: Backward Endcap EMC
1.– Requirements
2.– Geometry
3.- Summary
Distance target: from 560 to 520 mm
Inner Radius: from 150 to 128 mm
Angle trompet: 15,85º < 15,08º (30% smaller)
Wedge: One piece, cutting either 2 or 4 sides
Flange: At least 1000 mm from target
Summary

## Slide 14: Backward Endcap EMC
Personal Contact:
d.rodriguezpineiro@gsi.de
Tel: +49 (0) 6159171/1321
www.gsi.de
Thank you!